Lecture #14

- Recommendation for lab
  - Try to understand parameter block
  - Make sure we know how to write out the data and deal with parameter block
  - Read string from left to right just to make sure we understand it
    - Then try to read it from right to left
  - Just make sure we know how to read the data and write it to the output block

- .globl label
  - Used by linker to allow code from one file to use code from another file
  - In a C
    - Header file
      - int foo(int, int)
    - Two C files:
      - First
        - int x = foo(4, 5);
      - Second
        - int foo(int x, int x){
          - //code
        - }
  - In ASM
    - foo
    - Two files:
      - First
        - .global foo
        - jal foo
      - Second
        - .global foo
        - foo:
          - …
          - …
        - jal foo
  - Used for two things
    - External definition
      - Label you define that other ASM modules can use
    - External reference
      - Label you use but other files define
- Structures
  - struct foo{
    - int x;
    - int y;
    - int z;
  - } bar;
    - bar is an instance of the struct foo
    - bar.x = 1;
    - bar.y = 2;
    - bar.z = 3;
  - int x;
  - int *px = &x;
  - In ASM
    - bar:
      - .word 0
      - .word 0
      - .word 0
    - #t1 =1, t2=2. t3=3
    - la $t0, bar
    - sw $t1, 0($s0)
    - sw $t2, 4($s0)
    - sw $t3, 8($s0)
  - If we change the struct
    - struct foo{
      - int x;
      - char c;
      - int z;
    - }bar, b2;
    - Would be 12 bytes long in C
    - In ASM
      - bar:
        - .word 0
        - .byte 0
        - .align 2
        - .word 0
      - Load address and storing would be same, except the second sw would be sb
- Function calls
  - HLL
    - Return values – v0, v1
    - Parameters – a0, a1, a2, a3
      - Use structures if we need more than 4 parameters
    - callfunc – jal, jalr
    - ret – jr $ra
      - Can cause an infinite loop is a calls b, changes $ra to a, and then a returns to a
    - local var → scope ← parameters
      - s0 … s7