Lecture #8 & #9

- Array
  - Collection of data access none and index
    - Allele
      - Some type (length)
    - Continuous memory
      - Otherwise, we lose constant time access
    - Fixed size
  - EA = base + (index * len)
    - t0 = i * 4
    - EA = base + t0
- MIPS
  - Displacement address mode
    - imm (rs)
      - EA = rs + imm
    - Not designed to and does not help with array access (unless using a constant index)
- Swap function
  - swap (int[] a, int k)
    - int t = a[k]
    - a[k] = a[k+1]
    - a[k+1] = t
    - In MIPS
      - a0 is a, a1 is k
      - swap: #a0 = &a, a1 = k
        - mul $t0, $a1, 4
        - add $t1, $a0, $t0
        - lw $t2, 0($t1)	#$t2 = a[k]
        - lw $t3, 4($t1) #$t3 = a[k+1]
        - sw $t3, 0($t1)
        - sw $t2, 4($t1)
- ALU instructions (rd = rs op rt)
  - Fixed length instructions are good because they have a low CPI
    - Variable length instructions are good because they waste no bytes of memory for unneeded operands
  - 32 bit long instructions
    - 4 fields (R-type)
      - All operands are 5 bits long (15 total)
      - op-code is 6 bits, func is 6 bits
        - For R-type, is always 0
          - Then the lower 6 bits are the function op-code
          - This means that we only need to get rid of one op-code for I-types
        - Gives us 64 instructions
      - Remaining 5 bits are reserved for the shift amount
        - Used for sll, srl, sra (shift left logical, shift right logical, shift right arithmetic)
        - sll rd, rs, imm (immediate is unsigned here)
          - These take an immediate, but still are technically R-type codes
- Immediate instructions (rt = rs opp imm)
  - 32 bit long instructions
    - 4 fields (I-type)
      - rs and rt are 5 bits in length
      - imm is 16 bits
      - op-code is 6 bits
        - 63 instructions (lose one to R-type differentiation)
- 2 more pseudo-instructions we can use
  - move rd, rs
    - Used to copy value from one register to another
    - rd = rs
  - foo: 32 bit constant label
    - a is upper 16
    - b is lower 16 bits
    - a = foo >> 16
    - a = foo & 0xFFFF
    - Assembler can do arithmetic and bitwise operations on constants at assemble time
      - Use ‘C’ syntax
    - Goal is t0 with a in upper 16 and b in lower 16
      - addi $t0, $zero, foo >> 16
        - This gives us 16 0s in upper and a in lower
      - sll $t0, $t0, 16
        - This gives us a in upper, and 16 0s in lower
      - ori $t0, $t0, foo & 0xFFFF
        - This gives us a in upper, b in lower
      - We can make this 2, combining steps 1 and 2
        - load upper imm
          - Puts a 16 bit imm into upper 16 bits of a register
        - lui $t0, foo >> 16
    - load address combines 3 above steps
      - la rd, 32-bit const (which is almost always a label)
      - la $t0, foo
      - 2 instructions in reality
      - la $t0, 0($ao)
        - Example of how not to use la
        - Gets translated to this
          - addi $t0, $a0, 0
- change exec loc inst
  - Program counter
    - Point to instruction being executed
    - Point to next instruction to execute
  - Fetching instruction
    - If pointing to instruction being executed
      - pc = pc + 1
      - lw
    - If pointing to next instruction to execute
      - lw
      - pc = pc + 1
  - Fetch → decode → execute