Concepts of Computer Systems – Lecture #4

- Standard assembly line
  - Square brackets are option
  - [label:] [opcode [operand][, operand] …,] [# comment]
    - Label – symbolic representation corresponding to memory address where this will go
    - Kind of like a macro in C
  - Opcode – short English pneumonic corresponding to operation
    - Cannot have operand without an opcode
    - Up to 3 operands
  - # is comment symbol
    - No multi-line code symbols
  - Ex) foo: add $t0, $t1, $t2 #hi mom
- Standards guide
  - Lines cannot be over 80 characters in length
  - 8 space tabs
  - Label is always on the left-hand margin
    - Labels must be on the line above the code
  - Put a tab (8 spaces) before the opcode
  - One more tab between opcode and the first operand
    - No standard between individual operands, just be consistent
  - Comments start some amount of whitespace after the last operand
    - Comments should line up if possible, but there are exceptions
      - Comments in a single block of code should always be lined up
    - Comment long lines of code on the line above it
      - Newline, comment, code, newline
        - Line up comment with the rest of the code comments
    - Block comments started on left-hand margin
    - 1 tab for block comments that describe a block of code (not a function or file)
- MIPS belongs to a family referred to as load/store machines
  - Only instructions that can access memory are load and store instructions
    - Have to do more instructions to add things in memory
  - All instructions that do computation require all operands to be in registers
    - Use 3 operands

- Operations
  - Addition
    - add rd, rs, rt
      - rd = rs + rt
  - Subtraction
    - sub rd, rs, rt
      - rd = rs – rt
  - Bitwise And
    - and rd, rs, rt
      - rd = rs & rt
  - Bitwise Or
    - or rd, rs, rt
      - rd = rs | rt
  - Bitwise Nand
    - nand rd, rs, rt
    - Inversion of and
  - Bitwise Xor
    - xor rd, rs, rt
  - Bitwise Negation
    - not rd, rs
      - rd = ~rs
      - Same as nand rd, rs, rs
        - This is what the assembler does
    - Pseudo-instruction, which we can use
  - Addition/Subtraction/Bitwise are ALU instructions (Arithmetic & Logic Unit)
    - Logic means bitwise, since there is no boolean
  - i = i + 1 has to be two instructions, since we have to store 1 in memory
    - Solution to this is an “immediate value”, a constant stored in an instruction itself